## Slide 1: Chapter 1: Computer Networks and the Internet

## Slide 2: Roadmap
What is the Internet?
Network Edge
  end systems, access networks, links
Network Core
  packet switching, circuit switching, network structure
Delay, loss, throughput in networks
Protocol layers, Service models
Networks under attack: security
History

## Slide 3: What’s the Internet: “Nuts and Bolts”view
Internet : The Internet is a computer network that interconnects hundreds of millions of computing devices throughout the world
Hosts or End systems : Systems that are connected to Internet
Communication links : Coaxial cable, Copper wire, Optical fiber, and Radio spectrum
Transmission rate : measured in bits/second
Packet switches types : Routers and Link-layer switches
  Routers : Used in network core
  Link layer switches : Used in access networks

## Slide 4
Protocols : controls the sending and receiving of information within the Internet
Most important protocols in the Internet :
  Transmission Control Protocol (TCP)
  Internet Protocol (IP)
Internet standards are developed by the Internet Engineering Task Force (IETF)
The IETF standards documents are called requests for comments (RFCs)
There are currently more than 6,000 RFCs

## Slide 5: Some pieces of the Internet

## Slide 6: What’s the Internet : A Service View
An infrastructure that provides services to applications :
  electronic mail, Web surfing, social networks, instant messaging, Voiceover-IP (VoIP), video streaming, distributed games, peer-to-peer (P2P) file sharing, television over the Internet, remote login etc.
The applications are said to be distributed applications, since they involve multiple end systems that exchange data with each other.
End systems attached to the Internet provide an Application Programming Interface (API)
Internet API is a set of rules that the sending program must follow so that the Internet can deliver the data to the destination program.

## Slide 7: What is a Protocol
A protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of a message or other event.
A Human Analogy:
When people run different protocols, the protocols do not interoperate, and no useful work can be accomplished.
It takes two or more communicating entities running the same protocol in order to accomplish a task.

## Slide 8: A human protocol and a computer network protocol

## Slide 9: What is a Protocol
Network Protocols:
A network protocol is like a human protocol, except that the entities exchanging messages and taking actions are hardware or software components.
All activity in the Internet that involves two or more communicating remote entities is governed by a protocol.
Example:
  hardware-implemented protocols in two physically connected computers control the flow of bits on the “wire” between the two network interface cards
  congestion-control protocols in end systems control the rate at which packets are transmitted between sender and receiver
  protocols in routers determine a packet’s path from source to destination

## Slide 10: The Network Edge

## Slide 11: The Network Edge
End systems : the computers and other devices connected to the Internet
End systems include:
  desktop computers (e.g., desktop PCs, Macs, and Linux boxes),
  servers (e.g., Web and e-mail servers), and
  mobile computers (e.g., laptops, smartphones, and tablets).
Hosts are divided into two categories:
  Clients: desktop and mobile PCs, smartphones, etc.
  Servers: more powerful machines that store and distribute Web pages, stream video, relay e-mail, etc.

## Slide 12: End-system interaction

## Slide 13: The Network Edge : Access Networks
Access network:
  the network that physically connects an end system to the first router
First router is also known as the “edge router”

## Slide 14: Access Networks

## Slide 15: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite links
Two most prevalent types of broadband residential access are:
  Digital Subscriber Line (DSL) and
  Cable
Digital Subscriber Line
The residential telephone line carries both data and traditional telephone signals which are encoded at different frequencies:
  A high-speed downstream channel, in the 50 kHz to 1 MHz band
  A medium-speed upstream channel, in the 4 kHz to 50 kHz band
  An ordinary two-way telephone channel, in the 0 to 4 kHz band

## Slide 16: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite
Splitter: separates the data and telephone signals
DSLAM: separates the data and phone signals

## Slide 17: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite
Cable Internet access:
  makes use of the cable television company’s existing cable television infrastructure.
Fiber optics connect the cable head end to neighborhood-level junctions
Coaxial cable is then used to reach individual houses and apartments
Each neighborhood junction typically supports 500 to 5,000 homes

## Slide 18: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite
Cable modem termination system (CMTS):
  turning the analog signal sent from the cable modems in many downstream homes back into digital format.
A hybrid fiber-coaxial access network

## Slide 19: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite
FTTH(fiber to the home):
  up-and-coming technology that promises even higher speeds
Concept is to provide an optical fiber path from the CO directly to the home
FTTH Internet Access

## Slide 20: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite
Each home has an optical network terminator (ONT)
ONT is connected by dedicated optical fiber to a neighborhood splitter
The splitter combines several homes onto a single, shared optical fiber, which connects to an optical line terminator (OLT)
The OLT, providing conversion between optical and electrical signals, connects to the Internet via a telco router
In the home, users connect a home router to the ONT and access the Internet via this home router

## Slide 21: Home Access: DSL, Cable, FTTH, Dial-Up, and Satellite
In locations where DSL, cable, and FTTH are not available
  a satellite link can be used to connect a residence to the Internet at speeds of more than 1 Mbps
  StarBand and HughesNet are two such satellite access providers.
Dial-up access over traditional phone lines is based on the same model as DSL—a home modem connects over a phone line to a modem in the ISP.
Compared to other broadband access networks, dial-up access is extremely slow at 56 kbps.

## Slide 22: Access in the Enterprise (and the Home): Ethernet and WiFi
On corporate and university campuses, a LAN is used to connect an end system to the edge router
Ethernet is by far the most prevalent access technology in corporate, university, and home networks
Ethernet users use twisted-pair copper wire to connect to an Ethernet switch
With Ethernet access,
  users have 100 Mbps access to the Ethernet switch, whereas
  servers may have 1 Gbps or even 10 Gbps access.

## Slide 23: Access in the Enterprise (and the Home): Ethernet and WiFi
Ethernet Internet access

## Slide 24: Access in the Enterprise (and the Home): Ethernet and WiFi
In a wireless LAN setting:
  wireless users transmit/receive packets to/from an access point that is connected into the enterprise’s network which in turn is connected to the wired Internet
A typical home network

## Slide 25: Wide-Area Wireless Access: 3G and LTE
Telecommunications companies have made enormous investments in third-generation (3G) wireless, which provides wide-area wireless Internet access at speeds in excess of 1 Mbps.
Even higher-speed wide-area access technologies—a fourth-generation (4G) of wide-area wireless networks—are already being deployed.
LTE (Long-Term Evolution) has its roots in 3G technology and can potentially achieve rates in excess of 10 Mbps.

## Slide 26: Physical Media

## Slide 27: Physical Media
Physical medium can take many shapes and forms and does not have to be of the same type for each transmitter-receiver pair along the path.
Physical media fall into two categories:
  Guided media : the waves are guided along a solid medium
  Unguided media : the waves propagate in the atmosphere and in outer space
Examples of physical media include:
  twisted-pair copper wire,
  coaxial cable,
  multimode fiber-optic cable,
  terrestrial radio spectrum, and
  satellite radio spectrum.

## Slide 28: Twisted-Pair Copper Wire
Least expensive
Most commonly used
Used by telephone networks
Twisted pair consists of :
  two insulated copper wires,
  each about 1 mm thick,
  arranged in a regular spiral pattern.
  The wires are twisted together to reduce the electrical interference from similar pairs close by

## Slide 29: Twisted-Pair Copper Wire
Two Types :
UTP
  Commonly used for computer networks within a building, for LANs.
  Data rates for LANs using twisted pair today range from 10 Mbps to 10 Gbps.
STP
  Twisted pair cables incorporate shielding to prevent electromagnetic interference.

## Slide 30: Comparison Chart
BASIS FOR COMPARISON | UTP | STP
Basic | UTP (Unshielded twisted pair) is a cable with wires that are twisted together. | STP (Shielded twisted pair) is a twisted pair cable enclosed in foil or mesh shield.
Noise and crosstalk generation | High comparatively. | Less susceptible to noise and crosstalk.
Grounding cable | Not required | Necessarily required
Ease of handling | Easily installed as cables are smaller, lighter, and flexible. | Installation of cables is difficult comparatively.
Cost | Cheaper and does not require much maintenance. | Moderately expensive.
Data Rates | Slow comparatively. | Provides high data rates

## Slide 31: Coaxial Cable
Coaxial cable consists of two copper conductors, but the two conductors are concentric rather than parallel
High data transmission rates
Common in cable television systems
Coaxial cable can be used as a guided shared medium.

## Slide 32: Fiber Optics
An optical fiber is a thin, flexible medium
Conducts pulses of light, with each pulse representing a bit.
A single optical fiber can support tremendous bit rates, up to tens or even hundreds of gigabits per second
They are immune to electromagnetic interference
Have very low signal attenuation up to 100 kilometers
The Optical Carrier (OC) standard link speeds range from 51.8 Mbps to 39.8 Gbps
Standards in use today include OC-1, OC-3, OC-12, OC-24, OC-48, OC-96, OC-192, OC-768.

## Slide 33: Comparision
In transmitting electronic signals, attenuation is the loss of signal strength as measured in decibels (dB).

## Slide 34: Terrestrial Radio Channels
Radio channels carry signals in the electromagnetic spectrum
They require no physical wire to be installed
Provide connectivity to a mobile user
Characteristics of a radio channel depend significantly on the propagation environment and the distance

## Slide 35: Terrestrial Radio Channels
Terrestrial radio channels can be broadly classified into three groups :
  those that operate over very short distance (e.g., with one or two meters)
    wireless headsets, keyboards,
  those that operate in local areas, typically spanning from ten to a few hundred meters
    wireless LAN technologies
  those that operate in the wide area, spanning tens of kilometers
    cellular access technologies use wide-area radio channels

## Slide 36: Satellite Radio Channels
A communication satellite links two or more Earth-based microwave transmitter/ receivers, known as ground stations.
The satellite receives transmissions on one frequency band
Regenerates the signal using a repeater and
Transmits the signal on another frequency.
Two types of satellites are used in communications:
  Geostationary satellites and
  Low-earth orbiting (LEO) satellites.

## Slide 37: Satellite Radio Channels
Geostationary satellites permanently remain above the same spot on Earth
LEO satellites are placed much closer to Earth and do not remain permanently above one spot on Earth
They rotate around Earth

## Slide 38: The Network Core

## Slide 39: PACKET SWITCHING
In a network application, end systems exchange messages with each other
Messages may perform a control function or can contain data, such as an email message, a JPEG image, or an MP3 audio file
The source breaks long messages into smaller chunks of data known as packets
Each packet travels through communication links and packet switches
Packets are transmitted at a rate equal to the full transmission rate of the link
The time to transmit the packet is L/R seconds

## Slide 40: Packet-Switching: Store-and-Forward
Packet switches use store-and-forward transmission at the inputs to the links
Packet switch must receive the entire packet before it can transmit

## Slide 41: Packet-Switching: Store-and-Forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
end-end delay = N*L/R (assuming zero propagation delay)
routers need to receive, store, and process the entire packet before forwarding.
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec

## Slide 42: Packet Switching: queueing delay, loss
Each packet switch has multiple links attached to it
For each attached link, the packet switch has an output buffer/output queue
Output buffer : stores packets that the router is about to send into that link
Output buffer queuing delays : an arriving packet needs to be transmitted onto a link but finds the link busy, the arriving packet must wait in the output buffer
Delays are variable and depend on the level of congestion in the network
Packet loss — either the arriving packet or one of the already-queued packets will be dropped

## Slide 43: Packet switching

## Slide 44: Forwarding Tables and Routing Protocols
In the Internet, every end system has an address called an IP address
Each router has a forwarding table
Forwarding table : maps destination addresses to that router’s outbound links
Internet has a few special routing protocols that are used to automatically set the forwarding tables

## Slide 45: Forwarding Tables and Routing Protocols
Routing: determines source-destination route taken by packets
Forwarding: move packets from router’s input to appropriate router output
1
2
3
0111
dest address in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 46: CIRCUIT SWITCHING
Two fundamental approaches to moving data through a network of links and switches:
  Packet switching and
  Circuit switching
Circuit Switching : Resources needed for communication are reserved for the duration of the communication session
Traditional telephone networks are examples of circuit-switched networks

## Slide 47: A simple circuit-switched network consisting of four switches and four links
If each link between adjacent switches has a transmission rate of 1 Mbps
then each end-to-end circuit-switch connection gets 250 kbps of dedicated transmission rate.

## Slide 48: Multiplexing in Circuit-Switched Networks
A circuit in a link is implemented with either
  Frequency-division multiplexing (FDM) or
  Time-division multiplexing (TDM)
FDM
  The frequency spectrum of a link is divided up among the connections established across the link
  In telephone networks, this frequency band typically has a width of 4 kHz
  The width of the band is called the bandwidth
  FM radio stations also use FDM to share the frequency spectrum between 88 MHz and 108 MHz

## Slide 49: Multiplexing in Circuit-Switched Networks
TDM
  Time is divided into frames of fixed duration
  Each frame is divided into a fixed number of time slots
  When the network establishes a connection across a link, the network dedicates one time slot in every frame to this connection

## Slide 50: Multiplexing in Circuit-Switched Networks
The transmission rate of a circuit is equal to the frame rate multiplied by the number of bits in a slot
  Example : if the link transmits 8,000 frames per second and each slot consists of 8 bits, then the transmission rate of a circuit is 64 kbps.

## Slide 51: Circuit Switching Vs Packet Switching
For Data transmission, Packet Switching is the more efficient than Circuit Switching whereas,
When it comes to voice transmission Circuit switching is more efficient than packet switching.

## Slide 52: A NETWORK OF NETWORKS
End systems connect into the Internet via an access ISP
The access ISP can provide either wired or wireless connectivity
Using technologies including DSL, cable, FTTH, Wi-Fi, and cellular
The access ISPs themselves must be interconnected; this is done by creating a network of networks

## Slide 53: Network Structure 1
Interconnects all the access ISPs with a single global transit ISP
Global transit ISP is a network of routers and communication links that spans the globe
Global transit ISP also has at least one router near each of the hundreds of thousands of access ISPs
Since the access ISP pays the global transit ISP
the access ISP is said to be a customer and
the global transit ISP is said to be a provider
If a company builds a global transit ISP and is profitable then it’s natural for other companies to build their own global ISPs and compete with the original

## Slide 54: Network Structure 2
Consists of the hundreds of thousands of access ISPs and multiple global transit ISPs
The access ISPs certainly prefer Network Structure 2 over Network Structure 1
Based on pricing and service, ISPs can choose among competing Global transit ISPs
Global transit ISPs themselves must be interconnected :
  Otherwise access ISPs connected to one of the global transit providers would not be able to communicate with access ISPs connected to the other global transit provider

## Slide 55: A Network Of Networks
In any given region,
There may be a regional ISP to which the access ISPs in the region connect
Each regional ISP then connects to tier-1 ISPs
Tier-1 ISPs are like global transit ISP
Each access ISP pays the regional ISP, and regional ISP pays Tier-1 ISPs
There is customer-provider relationship at each level of the hierarchy

## Slide 56: A Network Of Networks
PoP : a group of one or more routers (at the same location) in the provider’s network
Internet Exchange Point (IXP) - typically in a stand-alone building with its own switches
There are roughly 300 IXPs in the Internet today

## Slide 57: Network Structure 5
The Internet of 2012
Network structure 5 builds on top of Network Structure 4 by adding content provider networks (Google)
Today’s Internet—a network of networks—is complex, consisting of a dozen or so tier-1 ISPs and hundreds of thousands of lower-tier ISPs

## Slide 58: Interconnection of ISPs

## Slide 59: Delay, Loss & Throughput in Packet-Switched Networks

## Slide 60: Overview of Delay in Packet-Switched Networks
A packet suffers several types of delays at each node along the path
Types of delays :
  Nodal processing delay,
  Queuing delay,
  Transmission delay, and
  Propagation delay
Together, these delays accumulate to give a total nodal delay

## Slide 61: Types of Delay
Processing Delay :
  time required to examine the packet’s header and determine where to direct the packet
Queuing Delay :
  at the queue/buffer, packet waits to be transmitted onto the link
Transmission Delay :
  amount of time required to push or transmit all of the packet’s bits into the link
Propagation Delay :
  time required to propagate from the beginning of the link to router B

## Slide 62: Comparing Transmission and Propagation Delay
Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
Car ~ bit
Caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
toll
booth
toll
booth
ten-car
caravan
100 km
100 km
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec = 2 min
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes

## Slide 63: Four Sources of a Packet Delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router

## Slide 64: Four Sources of a Packet Delay
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s

## Slide 65: Queueing delay (again)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
The ratio La/R, called the traffic intensity
La/R ~ 0: avg. queueing delay small
La/R > 1: avg. queueing delay large
La/R > 1: more“work”arriving
than can be serviced, average delay infinite!
La/R ~ 0
La/R -> 1

## Slide 66: Packet loss
Queue (or buffer) preceding a link has finite capacity
Packet arriving to full queue will be dropped (or lost)
Lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 67: End-to-End Delay
Suppose that the network is uncongested
  queuing delays are negligible
dtrans = L/R, where L is the packet size

## Slide 68: Traceroute
To get a hands-on feel for end-to-end delay, we can use the Traceroute program
Traceroute
  a simple program that can run in any Internet host

## Slide 69: Example
Output of a traceroute program :

## Slide 70: Throughput in Computer Networks
Instantaneous throughput at any instant of time is the rate (in bits/sec) at which Host B is receiving the file.
If the file consists of F bits and the transfer takes T seconds for Host B to receive all F bits
  then the average throughput of the file transfer is F/T bits/sec

## Slide 71: Throughput
the server cannot pump bits through its link at a rate faster than Rs bps
the router cannot forward bits at a rate faster than Rc bps
If Rs < Rc , throughput is Rs bps
If Rc < Rs , end-to-end throughput is Rc
Here, the throughput is min{Rc , Rs}, it is the transmission rate of the bottleneck link

## Slide 72: Throughput
A network with N links between the server and the client
Transmission rates of the N links being R1, R2,..., RN
Throughput for a file transfer from server to client is min{R1, R2,..., RN}

## Slide 73: Example motivated by today’s Internet
R is the transmission rate of the core link
All server access links have the same rate Rs
All client access links have the same rate Rc
If the rate of the common link, R, is large than both Rs and Rc
  the throughput for each download will be min{Rs , Rc }

## Slide 74: Protocol Layers And Their Service Models

## Slide 75: Introduction
There are many pieces to the Internet :
  numerous applications and protocols,
  various types of end systems,
  packet switches, and
  various types of link-level media
Question:
  is there any hope of organizing a network architecture?

## Slide 76: Layered Architecture
Human Analogy : Airline System
Taking an airplane trip: actions

## Slide 77: Layered Architecture
Each layer provides its service by :
  performing certain actions within that layer
  using the services of the layer directly below it
Horizontal layering of airline functionality

## Slide 78: Layered Architecture
A Layered Architecture
  a structured way to discuss system components
The system remains unchanged when a layer’s implementation is changed.
Note : changing the implementation of a service is very different from changing the service itself
The Internet protocol stack consists of five layers:
  the physical,
  link,
  network,
  transport, and
  application layers

## Slide 79: Protocol Layering
Network designers organize
  Protocols and
  The network hardware and software that implement the protocols — in layers
Taken together, the protocols of the various layers are called the protocol stack.

## Slide 80: Layers of the Internet Protocol Stack
Application Layer
Network applications and their application-layer protocols reside
Application Layer Protocols :
  HTTP protocol (for Web document request and transfer)
  SMTP (for the transfer of e-mail messages)
  FTP (for the transfer of files between two end systems)
An application-layer protocol is distributed over multiple end systems
packet of information at the application layer is a message

## Slide 81: Layers of the Internet Protocol Stack
Transport Layer
Transports application-layer messages between application endpoints
This layer provides :
  guaranteed delivery of messages to the destination and
  flow control
Two transport protocols :
  TCP
    breaks long messages into shorter segments
    provides a congestion-control mechanism
  UDP
    Provides a connectionless service to its applications
Transport-layer packet is a segment

## Slide 82: Layers of the Internet Protocol Stack
Network Layer
Responsible for moving datagrams from one host to another
Network Layer Protocol :
  IP Protocol
    defines the fields in the datagram as well as how the end systems and routers act on these fields
Network layer contains routing protocols that determine the routes
Network-layer packet is a datagram

## Slide 83: Layers of the Internet Protocol Stack
Link Layer
Responsible for moving entire frames from one network element to an adjacent network element
Services provided by the link layer depend on the specific link-layer protocol
Link Layer Protocols :
  Ethernet
  WiFi and
  the cable access network’s DOCSIS protocol
Link Layer packets are frames

## Slide 84: Layers of the Internet Protocol Stack
Physical Layer
Responsible for moving the individual bits within the frame from one node to the next
Protocols here are link dependent
Depends on the actual transmission medium of the link
  Example :
    twisted-pair copper wire
    single-mode fiber optics etc

## Slide 85: The OSI Model
Proposed in 1970s
ISO proposed that computer networks be organized around seven layers called the Open Systems Interconnection (OSI) model
The two additional layers present in the OSI reference model:
  Presentation layer : allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
  Session layer : synchronization, checkpointing, recovery of data exchange

## Slide 86: Encapsulation

## Slide 87: Encapsulation
Routers and Link-layer switches do not implement all the layers in the protocol stack
  they implement only the bottom layers
Internet routers can implement the IP protocol (a layer 3 protocol), while link-layer switches can not
Hosts implement all five layers

## Slide 88: Concept of Encapsulation
At the sending host, an application-layer message M is passed to the transport layer
The transport layer takes the message and appends additional information (so-called transport-layer header information, Ht )
The application-layer message and the transport-layer header information together constitute the transport-layer segment
The transport-layer segment thus encapsulates the application-layer message
At each layer
  a packet has two types of fields:
    header fields and
    a payload field
The payload is typically a packet from the layer above

## Slide 89: NETWORK SECURITY
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 90: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 91: Bad guys: attack server, network infrastructure
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
  select target
  break into hosts around the network (see botnet)
  send packets to target from compromised hosts

## Slide 92: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 93: Bad guys can use fake addresses
IP spoofing: send packet with false source address

## Slide 94: INTERNET HISTORY
1961-1972: Early packet-switching principles
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972: ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes

## Slide 95: INTERNET HISTORY
1972-1980: Internetworking, new and proprietary nets
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70s: proprietary architectures: DECnet, SNA, XNA
late 70s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture

## Slide 96: INTERNET HISTORY
1980-1990: new protocols, a proliferation of networks
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks

## Slide 97: INTERNET HISTORY
early 1990s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
1990, 2000’s: commercialization, the Web, new apps
late 1990s – 2000s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps

## Slide 98: INTERNET HISTORY
2005-present
~750 million hosts
  Smartphones and tablets
Aggressive deployment of broadband access
Increasing ubiquity of high-speed wireless access
Emergence of online social networks:
  Facebook: soon one billion users
Service providers (Google, Microsoft) create their own networks
  Bypass Internet, providing “instantaneous” access to search, emai, etc.
E-commerce, universities, enterprises running their services in “cloud” (eg, Amazon EC2)